iTopie RepRap
  Build Manual

---
CHAPTERS
The Frame
The X Axis
The Y Axis
The Z Axis
The Belts
The Heated Bed

---
CHAPTER 1
The Frame

---
Fit the rear
triangle on the U part.

---
Take a 3mm drillbit and adjuste
to 3.5mm from the mandrel.

---
Make some holes.
(4x)

---
Fit the assembly
on the O part.

---
Make more holes.
(4x)

---
Remove all parts and remake again
the holes in depth. (8x)

---
Ok !, Fit the feet
on the O part.

---
Turn back and... yes !
more and more holes. (4x)

---
Same as above, unplug the parts
and remake the holes. (4x)

---
The chamfers,
optional but recommended.
This is the back side

---
Glue and
screws party.

---
Apply some glue on
the two triangle.

---
Re-Fit the rear triangle on
the U part and press hard.

---
Turn back and screw all together
3.5x40mm (4x)

---
With a wet cloth,
wipe the superfluous glue.

---
Take the feet and
apply some glue.

---
Plug the feet and
press hard.

---
Turn back and screw all together
3.5x40mm (4x).

---
As before,
clean the glue.

---
Apply some glue
as pictured.

---
Fit all together
and press hard.

---
Turn back and screw all together
3.5x40mm (4x).

---
Do not forget to
clean the glue.

---
CHAPTER 1
The end...
At this point your frame is finished and functional. The following statement is optional but highly recommended.

---
1Cleaning, 2Apply some wood putty, 3Sanding,
4Final cleaning with a damp cloth.

---
5Color (two coats), 6Laquer (two coats), 7Logo.

---
CHAPTER 1
Alternative ending.